NEW SOFTWARE RELEASE
                          ====================

        Product involved:     AXIS HP-MIO

        Release date:         95-12-08

        Release type:         UPDATE

        Software version:     1.21

        Software media:       Prom 2 Mbit
                              or
                              File for flash loading.
                              See "read.me" file for loading.
                              This Flash file is only supported by
                              PCB version R1B.

        Software checksum:    Prom 2 Mbit:  223D

        Last preceding
        release:              1.20
        ---------------------------------------------------------------------

        Release Description:

        Changes since 1.20
        ==================

        - Sometimes software hang-up after PC-Host Sharing
          via MIO PC port or standard port on printer, corrected.

        - Interpretation of SCS-command SVF with default parameters
	  corrected. Problem with sometimes 'one line per page'
	  solved in 3287-emulation solved.

	- '0x' and '0X' might be used as an alternative to '$' when
	  writing hex-values in configuration-mode.

	- A new parameter, REINIT, can be set to YES to resend all
          settings to the printer if MIO timeout has expired. This
          solves the problem with certain LaserJets that changes
          their settings after their internal timeout.

        - HP-MIO can now be configured to use papersizes B4 and A3.

	- Sometimes the first page was printed in the wrong direction
	  and/or with wrong settings. Corrected.

	- The led labeled PC-SHARE is now turned off when the timeout
	  for the parallel port has expired.

	- A new parameter, TTMOUT, can be used in twinax mode to delay
	  the reporting when the printer goes off-line. It can be set
	  to values in the range 0-1000. 0 disables the reporting of
	  off-line while all other values are delay-times measured in
	  seconds.


	- Settings required to take advantage of color-printers are now
	  default.  Users without color-printers are not affected by
	  this.

	- Rare problem with text that was not printed solved.

	- Strings can now span over several lines in the parameter-list.

        Recommendation:

        - Change to this release if you want any of the features or
          have any of the problems mentioned above


        NOTE:

	-


        Best Regards,

        AXIS COMMUNICATIONS AB